Total Config size 4367:

set clock timezone 0

set vrouter trust-vr sharable

set vrouter "untrust-vr"

exit

set vrouter "trust-vr"

unset auto-route-export

exit

set auth-server "Local" id 0

set auth-server "Local" server-name "Local"

set auth default auth server "Local"

set auth radius accounting port 1646

set admin name "admin"

set admin password "nPV6LjrVF91Lcm6KXsiHsSKtjDMDVn"

set admin auth timeout 10

set admin auth server "Local"

set admin format dos

set zone "Trust" vrouter "trust-vr"

set zone "Untrust" vrouter "trust-vr"

set zone "Wzone1" vrouter "trust-vr"

set zone "VLAN" vrouter "trust-vr"

set zone "Untrust-Tun" vrouter "trust-vr"

set zone "Trust" tcp-rst

set zone "Untrust" block

unset zone "Untrust" tcp-rst

set zone "MGT" block

set zone "Wzone1" tcp-rst

set zone "VLAN" block

unset zone "VLAN" tcp-rst

set zone "Untrust" screen tear-drop

set zone "Untrust" screen syn-flood

set zone "Untrust" screen ping-death

set zone "Untrust" screen ip-filter-src

set zone "Untrust" screen land

set zone "V1-Untrust" screen tear-drop

set zone "V1-Untrust" screen syn-flood

set zone "V1-Untrust" screen ping-death

set zone "V1-Untrust" screen ip-filter-src

set zone "V1-Untrust" screen land

set interface "trust" zone "Trust"

set interface "wireless1" zone "Wzone1"

set interface "wireless2" zone "Trust"

set interface "untrust" zone "Untrust"

unset interface vlan1 ip

set interface trust ip 192.168.2.1/25

set interface trust nat

set interface wireless2 ip 192.168.2.129/25

set interface wireless2 nat

set interface untrust ip 192.168.100.160/24

set interface untrust route

unset interface vlan1 bypass-others-ipsec

unset interface vlan1 bypass-non-ip

set interface trust ip manageable

set interface wireless2 ip manageable

set interface untrust ip manageable

set interface untrust dhcp client enable

set interface trust dhcp server service

set interface wireless2 dhcp server service

set interface trust dhcp server auto

set interface wireless2 dhcp server auto

set interface trust dhcp server option gateway 192.168.2.1

set interface trust dhcp server option netmask 255.255.255.128

set interface trust dhcp server option dns1 192.168.100.1

set interface trust dhcp server option dns2 8.8.8.8

set interface wireless2 dhcp server option gateway 192.168.2.129

set interface wireless2 dhcp server option netmask 255.255.255.128

set interface wireless2 dhcp server option dns1 192.168.100.1

set interface wireless2 dhcp server option dns2 8.8.8.8

set interface trust dhcp server ip 192.168.2.20 to 192.168.2.120

set interface trust dhcp server ip 192.168.2.5 mac 00125a04591b

set interface trust dhcp server ip 192.168.2.6 mac 000f9093c992

set interface trust dhcp server ip 192.168.2.7 mac 003018a7e0d8

set interface wireless2 dhcp server ip 192.168.2.150 to 192.168.2.250

unset interface trust dhcp server config next-server-ip

unset interface wireless2 dhcp server config next-server-ip

set flow tcp-mss

unset flow no-tcp-seq-check

set flow tcp-syn-check

set pki authority default scep mode "auto"

set pki x509 default cert-path partial

set ike respond-bad-spi 1

unset ike ikeid-enumeration

unset ike dos-protection

unset ipsec access-session enable

set ipsec access-session maximum 5000

set ipsec access-session upper-threshold 0

set ipsec access-session lower-threshold 0

set ipsec access-session dead-p2-sa-timeout 0

unset ipsec access-session log-error

unset ipsec access-session info-exch-connected

unset ipsec access-session use-error-log

set url protocol websense

exit

set policy id 1 from "Trust" to "Untrust"  "Any" "Any" "ANY" permit log

set policy id 1

exit

set policy id 2 from "Untrust" to "Trust"  "Any" "Any" "ANY" deny log

set policy id 2

exit

set nsmgmt bulkcli reboot-timeout 60

set nsmgmt bulkcli reboot-wait 0

set ssh version v2

set config lock timeout 5

set modem speed 115200

set modem retry 3

set modem interval 10

set modem idle-time 10

set wlan channel auto

set ssid name splatspace

set ssid splatspace authentication wpa2-psk passphrase MVFy/j7hNM6g4XsL7HCUN1FqzTnlUR6q4g== encryption auto

set ssid splatspace interface wireless2

set snmp port listen 161

set snmp port trap 162

set vrouter "untrust-vr"

exit

set vrouter "trust-vr"

unset add-default-route

exit

set vrouter "untrust-vr"

exit

set vrouter "trust-vr"

exit